## Slide 1
Incident Response –
Protecting the Public
Public Health England
Workshop
xx/xx/xxxx

## Slide 2
Define the stages of incident response
Describe Response Phase for public protection
    Zoning
    Mass decontamination
    Shelter Vs Evacuation
Describe Risk Communication Approaches,
  Warning and informing
  Role of Social Media
Define Recovery Phase and key actions
Aims

## Slide 3
Incident Phases

## Slide 4
?
Key aspects to be determined will include.
Location of the incident?
  Quantity and type of chemicals involved?
  Location, numbers and types of receptors involved?
  Immediate threats are there casualties?
  Meteorological conditions?
  Resources available and timescales to mobilise these?
Initial risk assessment needs to be completed before response can be formulated.
A critical aspect of response is to obtain information on conditions on the ground.
Public Health Response - Initial Assessments
© ARCOPOL
© Hazrunoff

## Slide 5
If an incident occurs the immediate priorities will be to
  Make area safe (Zoning)
  Treat / decontaminate casualties
  Reduce wider exposure by advising people to leave affected areas (evacuation) or stay indoors (shelter in place)
  Protect sensitive ecosystems and infrastructure
Public Health Response - Immediate Actions
© ARCOPOL
©PHE

## Slide 6
Zoning is a specialised activity influenced by many factors such as the hazards involved, weather conditions, key receptors logistical issues.
Zoning
© ARCOPOL

## Slide 7
Zoning

## Slide 8: Mass Decontamination
To remove the hazardous substance and thus limit casualty exposure
To prevent secondary contamination of responders and public
Should be performed:
By skilled responders with appropriate personal protective equipment (PPE)
In the warm zone, upwind of the incident
Following removal of contaminated clothing from casualty - at the head working towards the toes
Using absorbent cloths and / or warm water (Rinse-wipe-rinse)
Determined on a chemical and incident (resource) specific basis.
© PHE

## Slide 9: Case Study – Graniteville
January 2005 - rail accident in South Carolina - tank cars of pressurised liquid chlorine ruptured.
The chemical rapidly vaporised on exposure to the atmosphere.
Chlorine - Hazards
Pale-green gas with characteristic odour - bleach.
Heavier than air so will keep low to the ground
Exposure to high concentrations may be fatal.
Minor exposures may result in burning sensation of the eyes and throat.
Moderate exposure may cause breathing difficulties.
Longer term may cause lung damage.
Powerful oxidising agent.
https://www.gov.uk/government/publications/chlorine-dioxide-incident-management

## Slide 10: Graniteville – Immediate Actions
Approximately 15 minutes - 300m exclusion “hot-zone” defined (Standard ERG Guidance).
Marshalling of firefighting personnel and equipment at a staging area upwind of the release site.
Within 50 minutes - decontamination stations organized upwind and at boundary of hot zone.
After 1 hour firefighter entry teams, wearing personal protective equipment entered the “Hot Zone”.
Triaged and casualties removed to one of the decontamination stations.
Nine people died, 72 were hospitalized, 525 were examined as outpatients.
5,400 residents within a mile of the crash site were forced to evacuate their homes.
Cevik et al. Mass casualties from acute inhalation of chlorine gas. Southern medical journal. 2009. Vol 102, No 12.

## Slide 11
Wider Population Protection - Sheltering
Often the default advice where there is risk of wider impacts (e.g. smoke or vapours):
  Go-in, Turn-on, Tune-in (to media sources)
  Keep doors and windows closed
  Close blinds and curtains if risk of explosion
  Turn off air condition / ventilation
  If necessary seal doors and windows with damp towels
  Use showers to knock-out gases if appropriate
  Ventilate properties when danger has passed

## Slide 12
  Sheltering will be helpful when the wind direction is changeable or buoyant but will not protect indefinitely
Figure. The movement of a plume at a given moment in time
© PHE
Sheltering - Considerations

## Slide 13
Wider Population Protection - Evacuation
Where sheltering cannot afford adequate protection.
Requires people to leave their homes / workplaces
Often used for non-residential situations e.g. workplace, outdoor scenarios.
Process needs to
Be co-ordinated with multiagency input
Be mindful of susceptible individuals e.g. young, elderly and infirm.
Have transport and reception facilities available
© Hazrunoff

## Slide 14
© PHE
May be logistically difficult
  Time of day
  Panic / Grid-locking
  Reluctance
May increase exposure
Therefore, normal advice to shelter.
Exceptions:
  Risk of fire/explosion
  Build up of dangerous levels
  Prolonged events
Evacuation - Considerations

## Slide 15: Case Study – Tyre Fire Wales - Wider Protection
June 2011 - fire at an unoccupied warehouse on an industrial estate in South Wales.
Source material comprised 5,000 tonnes of tyre ‘flock’
The fire continued to burn over the three-week period producing dense smoke.
Very quickly - Major incident declared.
A strategic coordination group (SCG) led by the local authority was established to provide risk assessment and incident management / Advice.
Key strategic decisions needed around risks to the public and the need for shelter and / or evacuation.
Real-time ambient air quality monitoring was implemented to assist in decision making .
https://assets.publishing.service.gov.uk/government/uploads/system/uploads/attachment_data/file/203631/CHaP_Report_21.pdf

## Slide 16: Should you stay or should you go?
Default public health advice - Shelter
Informed primarily by air monitoring.
But also
fire fighting activities,
meteorological forecasts,
logistics.
Public Health Outcomes
Communities up to 2 km from the incident (estimated population 24,812) potentially exposed.
98 health concerns reported during incident
Reports consistent with smoke exposure: coughs, sore throats, eye irritation, headaches and nausea.
https://uk-air.defra.gov.uk/air-pollution/daqi

## Slide 17: Banding is based upon specific chemical concentrations and exposure duration
https://uk-air.defra.gov.uk/air-pollution/daqi

## Slide 18
Clear mechanisms for effective and early communication. Forms an essential component of emergency planning, preparedness and response.
Getting Advice to the Public - Risk Communication
Risk communication
Crisis communication
Developed at the planning stage.
Predetermined materials regarding hazards and response.
Should be done in liaison with all stakeholders including local communities, businesses and action groups.
During an incident
Involving essential advice such as sheltering, evacuation, all-clear messages etc. via various media
© ARCOPOL

## Slide 19: Messages - Warning and Informing
What do you want the public to do?
Incident details:
- what has occurred
- who is in charge
- actions being taken
- who is at risk (from what, how)
- where to get further information
- where to get treatment / support
Simple, Timely, Accurate, Relevant, Credible, Consistent
Single source for communications usually the lead agency.
All forms of media
WHO Guidelines

## Slide 20: The Role of Social Media
Now an Essential means to monitor and disseminate messages
Free
Tweet deck provides “live” searches of key terms within defined geographical locations
Commercial Products
Many available
Search multiple platforms.
Real-time display to multiple users
Comprehensive data analytics
Alerts when detecting increased traffic
© Hazrunoff
https://www.brandwatch.com/
https://tweetdeck.twitter.com/
https://www.brandwatch.com/

## Slide 21
Also can obtain useful information from social media
Images and videos
Conditions “on the ground”
Timestamps, Geolocation
Responses / Emotions
© Hazrunoff

## Slide 22
Case Study – Essex Beach Incident
Busy beach during August bank holiday.
Beachgoers reported breathing difficulties following swimming / contact with sea water.
Police, ambulance and fire service attended. Public warned to stay out of the sea.
PHE further advice via local authority / NHS 111- shower and drink fresh water.
Multiple persons attended local hospital.
All affected persons recovered overnight.
Cause unknown – MCA - no evidence of spillage from vessels. Possibly marine algae – unconfirmed.

## Slide 23
Impact of PH messages – Essex Beach Incident – Day 1

## Slide 24
Essex Beach Incident – Day 2

## Slide 25: Ongoing Response
As the incident continues, focus will shift from the impacts on scene to the wider implications of exposure. It requires knowledge of
Pollutant behaviour in environment
Proximity of communities and ecosystems
Meteorological forecasts
Modelling forecasts
Monitoring and sampling
Provides a basis for continuously assessing and reviewing the risk to the public and the wider environment.
© ARCOPOL

## Slide 26
Recovery
Longer term actions following the incident
Victim support and follow-up – Physical and psychological treatment, aid for welfare, employment etc.
Remediation – Clean up of contamination
Restoration – Returning the environment to its original state
Rehabilitation – Adapting ways to get things back to normal
Investigation and applying lessons learnt
© ARCOPOL

## Slide 27
Further Useful Information / Materials
Manual for Public Health management of Chemical Incidents (WHO 2009) https://www.who.int/environmental_health_emergencies/en/
Arcopol Project – response tools / Risk Communications http://www.arcopol.eu/?/=/lang/en
Arcopol E-learning – Shoreline Response (guest log in)
http://www.cardiffmet.ac.uk/health/ITC/Pages/Public-Health-Management-for-Incidents-and-Events.aspx
Emergency Response Guidebook 2016 (US Dept of Transport) https://www.phmsa.dot.gov/hazmat/erg/emergency-response-guidebook-erg
Hazrunoff (Social Media study) http://www.hazrunoff.eu/tools-for-situation-awareness-emergency-response/
Uk Recovery Handbook for chemical incidents (UK HPA 2013) https://www.gov.uk/government/publications/uk-recovery-handbook-for-chemical-incidents-and-associated-publications
© ARCOPOL

## Slide 28
Questions?