## Slide 1
Hazard and Risk
Prioritisation and Assessment
Workshop
xx/xx/xxx

## Slide 2
Define the concepts of Hazard and Risk
Describe risk assessment process
    Source-Pathway-Receptor
Identify how hazards and risks may be prioritised
Present Hazrunoff hazard prioritisation approach
Present Hazrunoff Risk assessment tool
Aims

## Slide 3: Key Definitions
Hazard
Risk
“Any source of potential damage, harm or adverse effects”
“ The chance or probability that an adverse effect will occur”
A situation involving exposure to danger
Source Oxford English Dictionary
hazard is an inherent property it cannot be modified.

## Slide 4
can relate to both acute (immediate) and chronic (longer term) effects.
Mathematically it can be expressed as:
RISK* = Severity of Hazard x Probability of Exposure
(consequence) (Likelihood)
Risk Assessment
Process by which Risk(s) are characterized.
can be proactive (planning) and reactive (response).
vital to incident management.
*Risk also incorporates the extent of the effect and numbers affected.
Also influenced by perception

## Slide 5
Source-pathway-receptor approach
a source (Hazard) e.g. chemicals,
a receptor (e.g. people, ecological) that may be affected by the chemicals
a pathway for the chemical hazard to reach the receptor.
All 3 must be present to represent a risk.
Air dispersion & Atmospheric deposition
Evaporation, flotation, dissolve or sink
Pathways
Receptors
Source
Once viable S-P-R Linkages have been identified risks can then be assessed either by quantitative or qualitative judgement of severity and likelihood of exposure
© BBC

## Slide 6
Mitigate or control risk to a level deemed acceptable. Achieved by:
Breaking S-P-R linkages:
Reducing likelihood of an event:
Reducing severity of an event:
Where multiple hazards are identified it is not always possible to manage them all at once.
In such cases it is often useful to undertake prioritisation process enabling those hazards that pose the highest relative risk to be addressed first.
Risk Management
© Hazrunoff
© CEDRE

## Slide 7
Many coastal areas pose risks from former infrastructure such as landfills and industrial plant
Natural processes such as coastal erosion and flooding, can increase the potential for contaminants to impact health and the environment.
Not possible to provide contingencies for every eventuality.
Framework to prioritise chemical hazards, helping to focus resources on key pollutants
Hazrunoff Prioritisation Framework
© Hazrunoff

## Slide 8
An Illustration
© BBC

## Slide 9
An approach comprising two main elements
Desk based methodology to define:
  Scope – Temporal and geographical boundaries
  Source - key current and historical coastal activities / infrastructure:
  Pathway - Incorporating behaviour of pollutants with geological and hydrogeological \ hydrological factors
  Receptor – incorporating health, socio/economic and ecological factors
Database of key pollutants associated with industrial processes.
http://www.hazrunoff.eu/planning-training-and-exercising-for-response/

## Slide 10
Scoping – Where are we looking and why?
  Establishment of boundaries for proposed study area and time-frame for data searches.
  Determined by the assessor based upon the underlying objectives. No defined limits.
  Coastal erosion maps, flood zones, 5m contours are helpful indicators.
  Recommended to scope the area to a manageable size and if necessary use multiple assessments for large areas.

## Slide 11
Source – Pathway - Receptor
Past and current industrial infrastructure.
Human Health - populations, amenities
Socio-economic – transport, industry, agriculture / aquaculture
Environmental – rivers, aquifers
Ecological - habitats / species,
Tool can help identify pathways
No linkage = no risk
Determined from current and historical maps as well as records from regulatory bodies.
© Hazrunoff

## Slide 12
Prioritisation
Industry profile database, listing key pollutants from major industrial processes
Chemical database with assigned hazard scores.
Toxicity based upon GESAMP (Group of Expert Scientists for the Assessment of Marine Pollution)
Behaviour based upon the standard European behaviour classifications (SEBC).
Behaviour | Human Health | Ecological
Gas / Evaporator | 4 | 1
Floater | 3 | 2
Dissolver | 2 | 3
Sinker | 1 | 4

## Slide 13
Automated worksheets produce health and ecological prioritisations.
Can apply user defined weightings e.g. frequency of pollutant sources.
Displays results graphically for easy review
Prioritisation Tool

## Slide 14
Using the Results
Detailed risk assessments
Inform fate and transport models
Inform monitoring programmes
Develop contingency plans
Inform chemical data sheets
Develop Exercises and training

## Slide 15
Rapid risk assessment of Data
During an incident responders often have to evaluate large amounts of data.
Quickly process and display monitoring data.
Provide an initial assessment of results against health and / or ecological standards.
Estimate the significance of pollution – statistical analysis.
How?
This Photo by Unknown Author is licensed under CC BY-SA
© Hazrunoff

## Slide 16
The Water Risk Assessment Tool (WRAT)
Download from http://www.hazrunoff.eu/detecting-sensing-and-sampling/

## Slide 17
Design Specifications and Aims
Simple to use downloadable automated tool
No requirement for internet access
Accepts raw data from monitors (.txt, .xls and .csv)
Presents results in graphical and numerical outputs
Displays against relevant risk based thresholds / standards
  Drinking Water Standards
  Environmental Quality Standards
  Site specific limits
Indicates potential risks
© Hazrunoff
Notes: DWS – drinking water standards
EQS – Environmental quality standards
SNARLs - Suggested No Adverse Response Levels

## Slide 18
Import Data in xls or CSV format

## Slide 19
Results
Summary of data statistics
% samples failing to meet Trigger
Graphical Indication
Default or user defined Triggers
Up to 7 days Data processed in seconds

## Slide 20
Using the Results
Advise tactical and strategic co-ordination groups
  Immediate risks to health and / or environment
  Trends – is it rising or falling?
  Immediate Protective actions – populations, responders, environments
  Longer term impacts – food chain, ecology
© Twitter

## Slide 21
Questions?